iBus/DARC-Layer 6 used in Munich

Encoding: Latin-1
All Messages with the same Layer4-Channel-Nr. (50-75) belong to each other!!!

Station-Name Message:

000001 Always 0x000001
07b0 iBUS-ID
0037 Length of message after this in byte (0x0037 = 50)
2c Always 0x2c (message-type?)
02 Sequence-number
fd Always 0xfd
0cfa17 Some kind of bus-number and preamble-byte (But not for night-lines) (0x0B = Bus, 0x0C = Night?)
02 Sequence-number
00ffff Always 0x00ffff
03 Length of line-number (0x03 = 3)
4e3434 Line-number in ASCII (N44)
000129 Always 0x000129
02 Sequence-number
ef Always 0xef
15 Length till end of destination string (0x15 = 21)
26 Seems to be 0x20 + 3x sequence-number
13 Length of destination string (0x13 = 19)
484152524153202d204f53544241484e484f46 Destination string (HARRAS - OSTBAHNHOF)
2582 0x2580 + sequence-number
4602 0x4600 + sequence-number
0f810000 Always 0x0f810000
54 Position of slot in Time-Message (Byte-Offset)
0376330001 Always 0x0376330001 (if ASCII: EndOfTxt “v3”)

      0 1 2 3 4 5 6
Ch 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2
73 0x00000107b000322c00fd0b00350000ffff02353300012900ef11200f414944454e4241434853545241df45258046000f810000540376330001
73 5 3 A I D E N B A C H S T R A ß E
73 0x00000107b000292c01fd0b00350100ffff02353300012901ef082306484152524153258146010f810000540376330001
73 5 3 H A R R A S
73 0x00000107b000372c02fd0cfa170200ffff034e343400012902ef152613484152524153202d204f53544241484e484f46258246020f810000540376330001
73 N 4 4 H A R R A S - O S T B A H N H O F
73 0x00000107b200342c00fd0b00350000ffff02353300012900ef1320114ddc4e43484e4552204652454948454954258046000f810000600376330001
73 5 3 M Ü N C H N E R F R E I H E I T
71 0x0000010790002f2c02fd0b00390200ffff02353700012902ef0e260c4c41494d455220504c41545a258246020f810000360376330001
71 5 7 L A I M E R P L A T Z
71 0x000001079000332c03fd0b00380300ffff02353600012903ef12291046dc525354454e524945442057455354258346030f810000360376330001
71 5 6 F Ü R S T E N R I E D W E S T
Additional Station Message:

000001 Always 0x000001
0753 iBUS-ID
0026 Length of message after this in byte (0x0036 = 38)
2c002c04 Sequence-number of empty (or to be deleted) line-name/number
124e000076....02f730b8739 Always the same, absolutely no idea

53 0x000001061a0024124e0000760f000a7613000076180000730a8000730b800076141113730a902f730b8739
69 0x00000107610024124e0000760f000a7613000076180000730a8000730b800076141113730a902f730b8739
69 0x000001075d00262c00124e0000760f000a7613000076180000730a8000730b800076141113730a902f730b8739
56 0x000001065500282c002c04124e0000760f000a7613000076180000730a8000730b800076141113730a902f730b8739
55 0x000001065100262c02124e0000760f000a7613000076180000730a8000730b800076141113730a902f730b8739
55 0x000001064300262c01124e0000760f000a7613000076180000730a8000730b800076141113730a902f730b8739
69 0x000001075f00262c00124e0000760f000a7613000076180000730a8000730b800076141113730a902f730b8739
54 0x0000010631005e2c002c042c052c062c072c082c092c0a2c0b2c0c2c0d2c0e2c0f2c102c112c122c132c142c152c1
62c172c182c192c1a2c1b2c1c2c1d2c1e2c1f124e0000760f000a7613000076180000730a8000730b800076141113730a932a730b8634

Special-Message

000001 Always 0x000001
0753 iBUS-ID
0036 Length of message after this in byte (0x0036 = 54)
ef Always 0xef
31 Length till end of string (0x31 = 21)
28 0x22 + 3x sequence-number
2f Length of string (0x2f = 19)
5665727370....6e2e202b2b2b Message
4682 0x4680 + sequence-number
01 0x01 at most messages, sometimes 0x02,0x04 or 0x05 (Maybe a bit-field?)

68 0x00000107530036ef31282f5665727370e474756e6720647572636820737461726b6573205665726b656872736175666b6f6d6d656e2e202b2b2b468201
68 V e r s p ä t u n g d u r c h s t a r k e s V e r k e h r s a u f k o m m e n . + + +
72 0x00000107a4002cef2725255665727370e474756e6720776567656e2046616872747765677374f672756e672e202b2b2b468102
72 V e r s p ä t u n g w e g e n F a h r t w e g s t ö r u n g . + + +

Activator and Deactivator?? for Special-Message

000001 Always 0x000001
07a4 iBUS-ID
0003 Length of message after this in byte (0x0003 = 3)
4681 0x4680 + sequence-number (0x4600 for deactivation?), some kind of bit-field
03 Some kind of bit-field (seen between 0x01 and 0x06)

72 0x00000107a40003468103
72 0x00000107a40003468101

72 0x00000107a4000346010f

Time-Message:

0048 Length of message after this in byte (0x0048 = 72)
0040200c4018...020001472110 Time-Message (6byte for each display, byte offset referenced in Station-Name-Message)
 00480040200c4018000b2014401e000c20164020000c201c403003062311431b000a2014401e04062411441b04030009051004082412441c000b2015401f010621100014020001472110

One single Time-Message for one display:

 Display Line 1 | Display Line 2 | Display Line 3
00000100 00000011 00100100 00010000 00000010 00011010
| | | || |
| | | || \-> Time in Minutes
| | | |\-> Sometimes 1, maybe a flag for bus beeing late????
| | | \-> Always 0, 1 if slot is empty
| | \-> Reference to Station-Name-Message (Here: Show line-name and line-number of sequence 0x4)
| \-> Counter, if same line-name/number was shown in display line above (always 0 in display-line 1)
\-> Always 0, 1 if slot is empty

Almost empty message looks like:

0048e0e0e0e0e0e0e0e0e0e0e0e00161e0e0e0e0e0e0e0e0e0e0e0e0e0e0e0e0e0e0e0e0e0e0003ce0e0e0e00139e0e0e0e0003ce0e0e0e0e0e0e0e0e0e0e0e0e0e0e0e0e0e0e0e0e0eb

 Display Line 1 | Display Line 2 | Display Line 3
11100000 11100000 11100000 11100000 11100000 11100000

Absolutely no idea why the last byte of message is 0xeb instead of 0xe0...

Additional Special-Messagea:

56 0x0000010654001af11883ea011348616c74657374656c6c65207665726c65677403
56 H a l t e s t e l l e v e r l e g t
64 0x00000106f8001af1180ae9011348616c74657374656c6c65207665726c65677403
64 H a l t e s t e l l e v e r l e g t
55 0x0000010653001af118d646011348616c74657374656c6c65207665726c65677403
55 H a l t e s t e l l e v e r l e g t

000001 Always 0x000001
0654 iBUS-ID
001a Length of message after this in byte (0x001a = 26)
f1 Always 0xf1
18 Length till end of string (0x18 = 24)
83ea ???? Weird
01 Alwaya 0x01
12 Length of string (0x2f = 19)
48616c74657374656c6c65207665726c656774 Message
03 Always 0x03

55 0x0000010653001af118 d646 011348616c74657374656c6c65207665726c65677403
64 0x00000106f8001af118 0ae9 011348616c74657374656c6c65207665726c65677403
56 0x0000010654001af118 83ea 011348616c74657374656c6c65207665726c65677403
55 0x0000010653001af118 d646 011348616c74657374656c6c65207665726c65677403
56 0x0000010654001af118 83ea 011348616c74657374656c6c65207665726c65677403
64 0x00000106f8001af118 0ae9 011348616c74657374656c6c65207665726c65677403
55 0x0000010653001af118 d646 011348616c74657374656c6c65207665726c65677403
64 0x00000106f8001af118 0ae9 011348616c74657374656c6c65207665726c65677403
56 0x0000010654001af118 83ea 011348616c74657374656c6c65207665726c65677403

Gets sent in the mornig (about 7:00) maybe activate? Light Off?
52 0x00000106050008762400b4762500b4
51 0x00000105f10008762400b4762500b4